ST. JOSEPH’S COLLEGE (AUTONOMOUS), BANGALORE-27

B.Sc. CBCS – IV SEMESTER

END SEMESTER EXAMINATION: APRIL 2017

EL OE 4116 - Number System and Logic Circuits

# Time- 1 ½ hrs		        			                                    Max Marks-35

This paper contains THREE printed pages and THREE parts

PART-A

CHOOSE THE CORRECT ANSWER FROM THE OPTIONS GIVEN        10X01 = 10 Marks

- The octal equivalent of decimal number 127 is _____

- 177		b) 7F		c) 1111111		d) 77

- In BCD addition of two, two digit numbers 6 is added in the process of addition when ______

- When the sum of the nibble is greater than 15

- When the sum of the least significant nibble is greater than 9

- When the sum of least and most significant nibbles are greater than 9

- When the sum of the most significant nibble is greater than 9

- The keyboard of a present day computer is an example for ________ code

- 8421	b) Bar code		c) ASCII	d) Extended ASCII

- The next number in the counting of hexadecimal number 9AFEF is ______

- AB0F0	b) 9AFF0		c) 9B000		d) 9AFEE

- ____ is called an universal gate

- OR		b) AND		c) NAND		d) XOR

- The symbol for two input XNOR gate is __________

- IC ________ is a JK flip-flop

- 7400	b) 7486	c) 7476	d) 7490

- A decade counter needs _____ number of flip-flops

- 5		b) 4		c) 3		d) 10

- In the block diagram, the flip-flop is ______ triggering

- Level 	b) Negative edge 	c) Positive edge	d) Negative level

- The circuit given is a

- SISO shift register			c) 4 bit Asynchronous counter

- Johnson counter               	d) Ring counter

PART – B

- MATCH THE FOLLOWING                                                       5X1 = 5 Marks

| Gray code equivalent of 110111 | Flip-flop |
| --- | --- |
| Binary equivalent of 37 is | XOR gate |
| When all inputs are high we get output high | Counter |
| When odd number of inputs are high we get output high | 100101 |
| One bit memory device | AND gate |
|  | 101100 |

PART – C

ANSWER ANY TEN QUESTIONS                                                     10x2= 20 Marks

- Convert 255.5 into binary

- Subtract 27 from 120 using 2’s complement method.

- What is an ASCII code and mention its disadvantages over extended ASCII.

- What is an excess-3 code? Give an example.

- Write the circuit to obtain AND gate, its symbol and truth table.

- State De-Morgan’s theorems.

- Simplify the Boolean expression

- Write the output of the given circuit.

- Write the symbol of a positive edge triggered D flip-flop.

- Write the circuit of a 4 bit SISO shift register.

- Write the truth table for a 4 bit ripple up counter.

- Write a note on memory devices used.

**************************************

# Text boxes

Register Number:

DATE:   6-4-2017